## Slide 1: Master‘s Thesis Presentation
Richard Otto
Technical University of Munich
Department of Informatics
Chair of Robotics, Artificial Intelligence and Real-time Systems
Munich, 30. August 2019
Notes: Hallo,
I'm Richard and I'll presenting you an Overview about my Master Thesis
with the Title.............

## Slide 2: Autonomous Control for Wheel-less Snake Robot based on Neuromorphic Vision Sensor and Spiking Neural Network
Richard Otto
Supervisor: Prof. Dr.-Ing. habil. Alois Christian Knoll
Advisor: Zhuangyi Jiang
Munich, 30. August 2019

## Slide 3: Content
Motivation
Problem description
Setup
Training
Testing
Conclusion
Notes: The Content of my Talk subdivides in this Sections
...... so let's move on to the Motivaton

## Slide 4: Motivation
Autonomous robots have huge utilities:
  Search and Rescue
  Exploration
  Transportation
Key Ability: Real Time Navigation
Developments in Computer Science and Engineering make this goals reachable:
  More computational power
  New mathematical methods and models
  Improvements in sensors and hardware
Notes: special shapes, sizes help to performe better
and no humans are getting endangered
which is more and more reachable by developments....

## Slide 5: Problem description
Goal: Target tracking
Platform/Setup:
  Snake-like Robot
  Dynamic Vision Sensor
  Spiking Neural Network
  Neurorobotic Platform
Technique:
  R-STDP learning
Notes: task I try to solve in the thesis is a Target Tracking Task

## Slide 6: Robot
Snake-like Robot
Owned by Chair
Versatile Movement Options
Slithering Gait used
      Mimics biological movement
      Head faces in movement direction
      but moves from left to right
Z. Jiang [Jia18]
Notes: allowing vision by headmounted sensor

## Slide 7: Dynamic Vision Sensor
Tracks Change of Pixel Readings
Sends Event if Change overcomes Threshold
Event: <pixel_ID,event_Time,polarity>
Eventstream is served via a Bus by the Sensor
Advantages over Cameras:
    High temporal resolution
    Less overhead by not using Frames
    Resulting in less computational effort
      Less energy consumption
      Higher responsiveness
Notes: event is tuple of ......
polarity: direction of change ( undercut / exceeded )
great deal for autonomous systems
…goes along with Less Energy Consumption….

## Slide 8: Spiking Neural Network
Neurons:
    Leaky Integrate and Fire
    Model of biological Neuron
    Fires if Activation Level reaches Threshold
    Activation decays (Leak)
Synapses:
    Reward modulated STDP-Learning
    STDP-Learning used to update eligibility
    Dopamine level corresponds to the Reward

## Slide 9: Spiking Neural Network – R-STDP
R-STDP Mechanism (R. Legenstein [L08])

## Slide 10: Neurorobotics Platform
Used for simulating the Robot controlled by an SNN in a closed Loop
Controls SNN-Simulation and World Simulation
    Simulations are paused every 20ms
    Transfer Functions used for communication between the Simulations
Problem:
Simulated DVS Events all happen at the same time
Notes: Synchronizes simulations and handels their communication

## Slide 11: Neurorobotics Platform
J. Kaise [Kai+16]

## Slide 12: Neurorobotics Platform
Input Encoding:
    Spread events over the next timestep
    Crop input to relevant part
    Divide input into “Superpixels”
    Set Poisson Neuron to fire at a frequency corresponding to the number of events of its Superpixel:

## Slide 13: Neurorobotics Platform

## Slide 14: Neurorobotics Platform
Output Decoding:
    2 Neurons used
    Spikes of each get accumulated over last Timestep
    Direction given by:
Notes: output by 2 neurons

## Slide 15: Neurorobotics Platform
Reward:
    The Angle of the Head to the Target reflects the performance of the Robot
      Reward for the Output Neurons scales linear according to Angle:
      Dopamine Level of Synapses set according to the Reward
Notes: to train the network a reward function has to be choosen:

## Slide 16: Neurorobotics Platform
Reward Propagation:
  Reward unknown for Hidden Layer
  Rewards of the Output Layer has to be used
  Similar to the Backpropagation
  Simplification in this case:
Bing, Jiang [Bin+19]
Notes: reward can not be directly decided
reward for neuron:
weighted reward of all neurons it conncts to

## Slide 17: Training the Networks
Robot and Ball in empty Environment:
Ball Radius: 30cm
Distance: 1.6m
Ball movement in training:
  Eight like shape
  Ball faster than Robot
  Ball keeps distance and waits
  Track mirrored after each Reset

## Slide 18: Training the Networks - Basic Network
Topology of the Network
Notes: LIF Neurons necessary from Setup: Parrot incoming spikes

## Slide 19: Training the Networks - Basic Network
Performance of the Network

## Slide 20: Training the Networks - Basic Network
Plot of Weights in the Network

## Slide 21: Training the Networks - Adding Head Control
Topology of the Network

## Slide 22: Training the Networks - Adding Head Control
Performance of the Network

## Slide 23: Training the Networks - Adding Head Control
Additional Topologies:
  DVS & Head Output
  Joint Angles & Head Output
Training Results:
  Weights do not stabilize
  Networks unable to solve the task

## Slide 24: Training the Networks - Multi Layered
Topology of the Network

## Slide 25: Training the Networks - Multi Layered
Performance of the Network

## Slide 26: Training the Networks - Split Hidden Layer
Topology of the Network

## Slide 27: Training the Networks - Split Hidden Layer
Performance of the Network

## Slide 28: Testing
New Movement Pattern of Target:

## Slide 29: Testing – Basic Network
Solves without Fail
Good tracking of the Target
But high changes in the steering output

## Slide 30: Testing – Basic Network
Performance of the Network

## Slide 31: Testing – Multi Layered Network
Unable to solve
Drifting to the Right

## Slide 32: Testing – Multi Layered Network
Performance of the Network

## Slide 33: Testing - Split Hidden Layer
Solves without Fail
Very Good tracking of the Target
Body Angle to target comparable to Performance of Basic Setup
Control Signal much smoother

## Slide 34: Testing - Split Hidden Layer
Performance of the Network

## Slide 35: Conclusion
SNN capable of learning to Control Robot
Robust enough to handle Movement of Head
Single Layered Networks are not able to simultaneously control the direction of the Head and the Robot :
      Reduction of Information provided by DVS
      Information States not linear separable any more
      Multi Layered Network needed

## Slide 36: Conclusion
Bad Result of Multi Layered Network:
Network might not have reached a stable state in Training
Small weight changes in the hidden layer can have a amplified effect on the output
The topology of the multi layered Network can be reduced to the topology of the network with split hidden layer
Faster training of topologies designed for the task

## Slide 37: Future Work
Replace Network Controlling Head with more Complex Topology to enable Object detection
Duplicate DVS Layer to distinguish event Polarity

## Slide 38: Thank you for your attention!

## Slide 39
Questions?

## Slide 40: Sources
[JIA18] | Z. Jiang. Development and Control of a Bio-snake Robot. Oct. 2018.
[L08] | R. Legenstein, D. Pecevski, and W. Maass. “A learning theory for reward- modulated spike-timing-dependent plasticity with application to biofeed- back.” In: PLoS computational biology 4.10 (2008), e1000180.
[Kai+16] | J. Kaiser, J. C. V. Tieck, C. Hubschneider, P. Wolf, M. Weber, M. Hoff, A. Friedrich, K. Wojtasik, A. Roennau, R. Kohlhaas, et al. “Towards a framework for end-to-end control of a simulated vehicle with spiking neural networks.” In: 2016 IEEE International Conference on Simulation, Modeling, and Programming for Autonomous Robots (SIMPAR). IEEE. 2016, pp. 127–134.
[Bin+19] | Z. Bing, Z. Jiang, L. Cheng, C. Cai, K. Huang, A. Knoll, et al. “End to End Learning of a Multi-layered SNN Based on R-STDP for a Target Tracking Snake-like Robot, to be appear.” In: 2019 IEEE International Conference on Robotics and Automation (ICRA). 2019.

## Slide 41: Training the Networks - Adding Head Control
Plot of Weights in the Network

## Slide 42: Training the Networks - Multi Layered
Plot of Weights in the Network

## Slide 43: Training the Networks - Multi Layered
Plot of Weights in the Network

## Slide 44: Training the Networks - Split Hidden Layer
Plot of Weights in the Network